## Slide 1: CoreLab Update Future Internet Workshop
University of Tokyo/NICT
Aki NAKAO

## Slide 2
JGN
JGN2
Y2010 (Next Generation)
Y2015 (New Generation)
Current Network
Next Generation Network
(NXGN)
New Generation Network
(NWGN)
Collaboration of Industry, Academia and Government
International Competition and Collaboration
US (FIND, etc.)
EU (FP7, etc.)
Asia
NWGN Promotion Forum
Now
Before
JGN2plus
Toward the New Testbed
New Generation NW
(NWGN)
Activities toward NWGN
Service Platform Advanced Research Center
R&D of NWGN Service Middleware
Re-design of NWGN from scratch
Strategic advancement of R&D by collaboration of industry, academia and government
Social requirements for network
High speed, Diversity
High availability & quality
Secure, Energy saving
Action to unknown problem
PSTN
Cellular
Data NW
Global Trend toward NWGN
(FIND, FP7, etc.)
Cellular
PSTN
Internet
Improvement of international competitiveness
Next Generation NW
(NXGN)
Limit of existing technology
- Complexity by
added functions
- Limit of performance
improvement
NVLAB - Network Virtualization Research Lab
(UTokyo and NICT)
AKARI Project
JGN
JGN2
Y2010 (Next Generation)
Y2015 (New Generation)
Current Network
Next Generation Network
(NXGN)
New Generation Network
(NWGN)
Collaboration of Industry, Academia and Government
International Competition and Collaboration
US (FIND, etc.)
EU (FP7, etc.)
Asia
NWGN Promotion Forum
Now
Before
JGN2plus
Toward the New Testbed
New Generation NW
(NWGN)
Activities toward NWGN
Service Platform Advanced Research Center
R&D of NWGN Service Middleware
Re-design of NWGN from scratch
Strategic advancement of R&D by collaboration of industry, academia and government
Social requirements for network
High speed, Diversity
High availability & quality
Secure, Energy saving
Action to unknown problem
PSTN
Cellular
Data NW
Global Trend toward NWGN
(FIND, FP7, etc.)
Cellular
PSTN
Internet
Improvement of international competitiveness
Next Generation NW
(NXGN)
Limit of existing technology
- Complexity by
added functions
- Limit of performance
improvement
NVLAB - Network Virtualization Research Lab
(UTokyo and NICT)
AKARI Project
JGN
JGN2
Y2010 (Next Generation)
Y2015 (New Generation)
Current Network
Next Generation Network
(NXGN)
New Generation Network
(NWGN)
Collaboration of Industry, Academia and Government
International Competition and Collaboration
US (FIND, etc.)
EU (FP7, etc.)
Asia
NWGN Promotion Forum
Now
Before
JGN2plus
Toward the New Testbed
New Generation NW
(NWGN)
Activities toward NWGN
Service Platform Advanced Research Center
R&D of NWGN Service Middleware
Re-design of NWGN from scratch
Strategic advancement of R&D by collaboration of industry, academia and government
Social requirements for network
High speed, Diversity
High availability & quality
Secure, Energy saving
Action to unknown problem
PSTN
Cellular
Data NW
Global Trend toward NWGN
(FIND, FP7, etc.)
Cellular
PSTN
Internet
Improvement of international competitiveness
Next Generation NW
(NXGN)
Limit of existing technology
- Complexity by
added functions
- Limit of performance
improvement
NVLAB - Network Virtualization Research Lab
(UTokyo and NICT)
AKARI Project
JGN
JGN2
Y2010 (Next Generation)
Y2015 (New Generation)
Current Network
Next Generation Network
(NXGN)
New Generation Network
(NWGN)
Collaboration of Industry, Academia and Government
International Competition and Collaboration
US (FIND, etc.)
EU (FP7, etc.)
Asia
NWGN Promotion Forum
Now
Before
JGN2plus
Toward the New Testbed
New Generation NW
(NWGN)
Activities toward NWGN
Service Platform Advanced Research Center
R&D of NWGN Service Middleware
Re-design of NWGN from scratch
Strategic advancement of R&D by collaboration of industry, academia and government
Social requirements for network
High speed, Diversity
High availability & quality
Secure, Energy saving
Action to unknown problem
PSTN
Cellular
Data NW
Global Trend toward NWGN
(FIND, FP7, etc.)
Cellular
PSTN
Internet
Improvement of international competitiveness
Next Generation NW
(NXGN)
Limit of existing technology
- Complexity by
added functions
- Limit of performance
improvement
NVLAB - Network Virtualization Research Lab
(UTokyo and NICT)
AKARI Project
JGN
JGN2
Y2010 (Next Generation)
Y2015 (New Generation)
Current Network
Next Generation Network
(NXGN)
New Generation Network
(NWGN)
Collaboration of Industry, Academia and Government
International Competition and Collaboration
US (FIND, etc.)
EU (FP7, etc.)
Asia
NWGN Promotion Forum
Now
Before
JGN2plus
Toward the New Testbed
New Generation NW
(NWGN)
Activities toward NWGN
Service Platform Advanced Research Center
R&D of NWGN Service Middleware
Re-design of NWGN from scratch
Strategic advancement of R&D by collaboration of industry, academia and government
Social requirements for network
High speed, Diversity
High availability & quality
Secure, Energy saving
Action to unknown problem
PSTN
Cellular
Data NW
Global Trend toward NWGN
(FIND, FP7, etc.)
Cellular
PSTN
Internet
Improvement of international competitiveness
Next Generation NW
(NXGN)
Limit of existing technology
- Complexity by
added functions
- Limit of performance
improvement
NVLAB - Network Virtualization Research Lab
(UTokyo and NICT)
AKARI Project
JGN
JGN2
Y2010 (Next Generation)
Y2015 (New Generation)
Current Network
Next Generation Network
(NXGN)
New Generation Network
(NWGN)
Collaboration of Industry, Academia and Government
International Competition and Collaboration
US (FIND, etc.)
EU (FP7, etc.)
Asia
NWGN Promotion Forum
Now
Before
JGN2plus
Toward the New Testbed
New Generation NW
(NWGN)
Activities toward NWGN
Service Platform Advanced Research Center
R&D of NWGN Service Middleware
Re-design of NWGN from scratch
Strategic advancement of R&D by collaboration of industry, academia and government
Social requirements for network
High speed, Diversity
High availability & quality
Secure, Energy saving
Action to unknown problem
PSTN
Cellular
Data NW
Global Trend toward NWGN
(FIND, FP7, etc.)
Cellular
PSTN
Internet
Improvement of international competitiveness
Next Generation NW
(NXGN)
Limit of existing technology
- Complexity by
added functions
- Limit of performance
improvement
NVLAB - Network Virtualization Research Lab
(UTokyo and NICT)
AKARI Project
JGN
JGN2
Y2010 (Next Generation)
Y2015 (New Generation)
Current Network
Next Generation Network
(NXGN)
New Generation Network
(NWGN)
Collaboration of Industry, Academia and Government
International Competition and Collaboration
US (FIND, etc.)
EU (FP7, etc.)
Asia
NWGN Promotion Forum
Now
Before
JGN2plus
Toward the New Testbed
New Generation NW
(NWGN)
Activities toward NWGN
Service Platform Advanced Research Center
R&D of NWGN Service Middleware
Re-design of NWGN from scratch
Strategic advancement of R&D by collaboration of industry, academia and government
Social requirements for network
High speed, Diversity
High availability & quality
Secure, Energy saving
Action to unknown problem
PSTN
Cellular
Data NW
Global Trend toward NWGN
(FIND, FP7, etc.)
Cellular
PSTN
Internet
Improvement of international competitiveness
Next Generation NW
(NXGN)
Limit of existing technology
- Complexity by
added functions
- Limit of performance
improvement
NVLAB - Network Virtualization Research Lab
(UTokyo and NICT)
AKARI Project
JGN
JGN2
Y2010 (Next Generation)
Y2015 (New Generation)
Current Network
Next Generation Network
(NXGN)
New Generation Network
(NWGN)
Collaboration of Industry, Academia and Government
International Competition and Collaboration
US (FIND, etc.)
EU (FP7, etc.)
Asia
NWGN Promotion Forum
Now
Before
JGN2plus
Toward the New Testbed
New Generation NW
(NWGN)
Activities toward NWGN
Service Platform Advanced Research Center
R&D of NWGN Service Middleware
Re-design of NWGN from scratch
Strategic advancement of R&D by collaboration of industry, academia and government
Social requirements for network
High speed, Diversity
High availability & quality
Secure, Energy saving
Action to unknown problem
PSTN
Cellular
Data NW
Global Trend toward NWGN
(FIND, FP7, etc.)
Cellular
PSTN
Internet
Improvement of international competitiveness
Next Generation NW
(NXGN)
Limit of existing technology
- Complexity by
added functions
- Limit of performance
improvement
NVLAB - Network Virtualization Research Lab
(UTokyo and NICT)
AKARI Project
Research Activity on Future Internet

## Slide 3
R&D for defining and designing future Internet
Network Virtualization Research Lab
(UTokyo+NICT)
CoreLab (UTokyo+NICT)
AKARI Architecture Design Project
(NICT+Universities)
SPARC Service Middleware Project(NICT)
JGN2Plus Test-bed(NICT)
Overview of Research on NwGN
Network Vitualization as Architecture
and its applications !!
Today’s Talk

## Slide 4: Network Virtualization as Architecture
Isolate physical network resources through virtualization and hold multiple independent and programmable logical networks
  Implement multiple network architectures and services on top of isolated logical networks
    Meta-architecture to enable multiple architectures
    Testbed technology for a new architecture
  Operate multiple existing architectures
    Dynamic and secure logical networks
    User- and application specific logical networks
    New business models for carriers and operators

## Slide 5: A Step Towards Reality: PlanetLab Enhancement
The largest and most popular overlay network test-bed
Currently consists of 900+ nodes at 450+ sites
800+ Projects/ 1000+ Researchers
  180+ high-level academic publications enabled

## Slide 6: What have we learned from PlanetLab?
Concept
  Slice-based experimental facility
“Slice” Mechanism
  Resource Isolation through Virtualization
Management Framework
  Node : Physical Machine
  Sliver : Virtual Machine
  Slice : A collection of Virtual Machines
  RSpec: Resource Description
  PLC: Central Management Servers

## Slide 7: Limitations in PlanetLab
Flexibility is sacrificed over Scalability/Performance
  Sliver : Container-based Resource Isolation
  Shares crucial resources
    Single kernel (Linux with VServer patch)
    Network stack and modules (NAT, Firewall, etc)
    Network resources (IP address and ports)
    Vnet (virtual network device ; need work for multi-homing)
  Cannot run arbitrary kernel/network stack & modules

## Slide 8: Design Principle for a New Test-bed
Performance
  Network I/O
Scalability
  The number of slices
Isolation
  Resource must be isolated per slice
Flexibility
  Arbitrary kernel/network stacks/resources

## Slide 9: CoreLab Update
Design
  Sliver VEE : Hosted VMM + Resource Container
  Introducing Flexibility in execution environment
  VM Disk Image Transfer : Multipath & Caching
  Network Configuration : Multihoming
  Management Tools: Reuse PlanetLab’s design
  Federation with PLC, OneLab2, VINI, Max, G-Lab
Comparison Chart | PlanetLab | CoreLab
Sliver | Resource Container | Hosted VMM
Kernel | Shared | Separated
Guest OS | Various Linux Distros | Any OSes
IP & Port | Shared | Shared (managed)
Privileged System Calls | Shared | Isolated
New

## Slide 10: VEE Candidate for Sliver Implementation
Design Principles | Performance | Scalability | Security Isolation | Performance Isolation | Flexibility | Code Reusability
Resource Container | + | + |  | + | - | 
Hyper- visor | + |  | + | + | + | -
Hosted- VMM | ? | ? | + | ? | + | +
Hardware
VMM
VM
VM
GuestOS
GuestOS
Apps
apps
VM
MngOS
Manager
Hypervisor-Based
Hardware
HostOS
Apps
VM
VM
GuestOS
GuestOS
Apps
Apps
Host-Based
Hardware
HostOS
Apps
VE
VE
Apps
Apps
Resource Container
advantageous
disadvantageous
room for improvement
Supported by CoreLab
Supported by CoreLab

## Slide 11: CoreLab Deployment (on-going)
Phase1 : 12 Sites over JGN2Plus + SINET + others
Phase1.1: Support Various Virtualization Technologies
Phase1.2: More nodes deployed in Japan (+12)
Phase2 : Extend to Asian Region
HP DL 580 (4U)
Intel Xeon 16-core (quad 4-core)
128GB (Max 256GB) memory
300GB RAID5
(accommodate up to 254 slices)

## Slide 12: CoreLab : In Action…
http://www.corelab.jp

## Slide 13: Phase 1.1 Update
New Features
  Framework to support various virtualizations
    OpenVZ (Resource Containers)
    KVM (Hosted Virtualization)
    Xen (Hypervisor) (planned…)
  Supporting various OS types
    Linux multi-kernel support
    Windows (para virtualization coming soon…)
  Network namespace reservation
    Slice-wide namespace (port) reservation
  Resource control
    Cgroups, TC, etc
  Node Logging
    Keeping track of events from nodes

## Slide 14: CoreLab Admin Interface (Update)
Manage Node Type
OVZ, KVM,
VM Images
Linux Distros, Windows
Node Logs / Events
Notifications & Errors
Resource Control
Slice-Wide Namespace Reservation
Things not shown here….

## Slide 15: Registering/Selecting VM Images
Fedora10 (RedHat Type/ i386)
We can add arbitrary VM images to disseminate to nodes…

## Slide 16: Slice-wide Port Reservation
Flash Interface to reserve
Port range for a slice
Port Range to be assigned
To a new KVM slice…
Port Range already assigned
to the other slices

## Slide 17: Creating A Slice…
VM Image
Arbitrary OS images registered
VM Type
KVM, LXC, OVZ, and more coming
Multihome
SINET, JGN2Plus, or both
NIC Model
Vanilla, Para-Virtualized Drivers
Memory Size
256, 512, 1024, 4096, 8192 MB
Suspend Feature
Suspend the slice when idol

## Slide 18: Slices in Action…
In this example,
there are three slices running in our test CoreLab PLC
One OVZ and Two KVM slices

## Slide 19: Conclusions
Network Virtualization is one of the most important visions
Enabling infrastructure for NetVirt is already taking place
Applications of network virtualization are very important..

## Slide 20: Contact Information
Network Virtualization is one of the key technologies for proceeding further in defining NwGN architecture(s)
We are turning this vision into reality..
Net-Virtualization Research Lab Contact: nakao@iii.u-tokyo.ac.jp
nv-lab@ml.nict.go.jp
http://www.nvlab.org